## Slide 1
Computer Networks · Final Project
VANISHING
ADDRESS
Moving Target Defense via OpenFlow Random Host Mutation
SDN · OpenFlow 1.3 · Ryu Controller · Mininet · Raspberry Pi 5 · GPIO LEDs

## Slide 2
The Paper Behind This (Introduction)
We didn't invent the idea — we built on top of existing research and pushed it further.
ACM HotSDN 2012
OpenFlow Random
Host Mutation
Jafarian, Al-Shaer & Duan
The core idea:
Hosts have hidden real IPs (10.0.0.x)
The network exposes rotating virtual IPs to the outside
Virtual IPs (VIPs) change on a timer — every 30–60 seconds
Attacker scans the network... but the map goes stale
An SDN controller manages all VIP ↔ real IP mapping
How the attacker gets tricked
ATTACKER
nmap 172.16.0.0/16
sees →
VIP
172.16.44.7
controller
routes to
SDN CONTROLLER
Knows: VIP 172.16.44.7 = real host 10.0.0.2
REAL HOST — h2
10.0.0.2
Every 30s VIPs rotate → attacker's scan data is worthless

## Slide 3
What We Add On Top (Motivation)
The paper proved the concept. We made it real, reactive, and physical.
Our Addition
Reactive Scan Detection
If an attacker probes 3+ different VIPs within 10 seconds, the controller declares a scan and triggers emergency rotation immediately — not just on a timer. The original paper only does scheduled rotation.
Implementation Fix
TCP Monitoring Flows
Once NAT flows are installed, packets never hit the controller — scan tracking would silently break. We added a higher-priority OpenFlow rule that copies each TCP packet to the controller before NAT rewrites it, so we see the original destination VIP.
Hardware
Physical Hardware on Pi 5
The 2012 paper was simulation only. We deployed the entire system on a Raspberry Pi 5 running Open vSwitch — a real, functioning prototype you can hold in your hand.
Hardware
GPIO LED Attack Indicators
Yellow LED (GPIO 17) blinks on every scheduled rotation. Red LED (GPIO 27) blinks 3× rapidly when a scan is detected. Physical, visible proof the defense is actively working.

## Slide 4
What is SDN?
Software Defined Networking — separating the "brain" of a network from the "muscle".
Traditional Router
Control Plane
Decides where packets go
(routing table, forwarding logic)
Data Plane
Physically moves packets
(hardware, ASICs, ports)
Both planes locked in the same box.
You cannot reprogram it from outside.
→
SDN
splits
these
Software Defined Networking (SDN)
Control Plane — Controller
Runs on a server. Your code lives here.
→ Ryu Controller (Python)
OpenFlow
protocol
Data Plane — OVS Switch
Just does what the controller tells it.
Fast, dumb, and reprogrammable.
The layer we add:
Our Ryu controller intercepts ARP, hands out VIPs, rewrites OpenFlow tables in the OVS switch every 30s, and detects scans. The switch enforces it all — hosts never know VIPs exist.

## Slide 5
Software Simulation
Runs on a Linux machine (or WSL2). No hardware needed — a full virtual network in software.
Ryu Controller
controller.py
Our Python SDN app. Manages VIP assignments, installs OpenFlow flows, detects scans, triggers rotation.
Mininet
topology.py
Creates a virtual network of hosts and a switch on your laptop — no physical hardware needed.
Open vSwitch
(via Mininet)
A software OpenFlow switch. Receives flow rules from Ryu and enforces all NAT rewrites.
Nmap (Attacker)
demo.py
The scanner. Sweeps the VIP subnet to discover hosts. Runs twice to prove addresses have changed.
Demo Script
demo.py
Orchestrates the whole scenario: warmup → scan #1 → wait for rotation → scan #2 → compare.
What the demo does, step by step
Warmup
Hosts ping each other. Controller learns MACs, assigns VIPs. Ryu installs NAT flows in OVS.
Scan #1
nmap sweeps 172.16.0.0/16. Discovers 3 active VIP addresses. This is what the attacker knows.
Rotation
Timer fires (30s). All VIPs change. OVS flow tables are rewritten. Yellow LED blinks on Pi.
Scan #2
nmap sweeps again. Returns completely different IPs. Zero overlap with scan #1.
Verify
h1 still pings h2 using the new VIP. Legitimate traffic is unaffected by the defense.
Result
PASS: attacker's scan data is 100% wrong. MTD is working. Defense is transparent to real users.

## Slide 6
PROJECT TEMPLATE

## Slide 7
The Hardware Demo
Taking the simulation off the laptop and onto a real device — with LEDs that blink when something happens.
Components
Raspberry Pi 5
The entire MTD system runs here — Open vSwitch + Ryu Controller + our Python code.
Open vSwitch (OVS)
Software OpenFlow switch on the Pi. Enforces the NAT flow rules sent by Ryu.
Yellow LED (GPIO 17)
Blinks once on every scheduled VIP rotation. Visual pulse of the defense working.
Red LED (GPIO 27)
Blinks 3× rapidly when a scan is detected. Physical alarm for an active attack.
330Ω Resistors
One per LED, wired to GND. Protects the Pi from blowing the GPIO pins.
What you'll see on demo day
System boots
Pi connects to WiFi. Ryu starts. VIPs assigned to all hosts automatically.
SCAN
Attack begins
Attacker runs nmap. Discovers 3 VIPs. Red LED blinks 3× — scan detected.
BLINK
Rotation event
Yellow LED blinks once. All VIPs change. OVS flow tables rewritten instantly.
SCAN
Scan again
nmap returns completely different VIPs. Zero overlap with the first scan.
OK
Legit traffic
h1 pings h2 using the new VIP — works fine. Defense is invisible to real users.

## Slide 8
Literature Review (1 / 2)
Direct predecessors — papers we build upon and explicitly extend.
Paper & Venue | Core Idea | Gap / What We Add
"OpenFlow Random Host Mutation: Transparently Moving Target Defense using SDN" Jafarian, Al-Shaer & Duan ACM HotSDN, 2012 | First SDN-based MTD via IP rotation. Controller assigns VIPs to real hosts and installs a 2-table OpenFlow NAT pipeline. ARP proxy handles VIP resolution. VIPs rotate on a fixed timer. | No scan detection — rotation is purely scheduled. Simulation only; no physical deployment. TCP monitoring for scan visibility post-NAT is absent. No reactive emergency rotation.
"Toward Network Configuration Randomization for Moving Target Defense" Al-Shaer, E. Springer — Moving Target Defense, 2011 | Framework for randomizing IPs, ports, and protocols simultaneously to create unpredictable attack surface. Defines theoretical metrics for measuring randomization effectiveness. | Purely theoretical — no SDN or OpenFlow implementation. No scan detection or reactive rotation. Randomization model not validated on a live network or embedded hardware.
"MT6D: A Moving Target IPv6 Defense" Dunlop, Groat, Marchany & Tront IEEE MILCOM, 2011 | Applies MTD to IPv6 by randomizing host addresses on a schedule. Leverages IPv6 stateless autoconfiguration. Makes scanning ineffective by constantly shifting the address space. | IPv6 only — not applicable to IPv4/SDN environments. No OpenFlow or controller-based NAT. No scan detection or emergency rotation. No hardware deployment on embedded systems.
"SDN-based Solutions for Moving Target Defense Network Application" Kampanakis, Perros & Beyene IEEE WoWMoM, 2014 | Uses SDN to implement IP and port randomization. Evaluates performance overhead of randomization schemes in an SDN environment. Demonstrates controller-managed mutation is feasible. | No 3-table OpenFlow pipeline or TCP monitoring flow for scan visibility. No scan detection or emergency rotation. No physical hardware or embedded system deployment.

## Slide 9
Literature Review (2 / 2)
Broader MTD foundations — theoretical frameworks and optimization approaches.
Paper & Venue | Core Idea | Gap / What We Add
"Frequency-Minimal Moving Target Defense using Software-Defined Networking" Debroy, Calyam & Nguyen IEEE ICNC, 2016 | Optimizes IP mutation frequency to minimize network overhead while preserving defense quality. Proposes adaptive rotation intervals based on attack probability and network load. | Focuses only on scheduling optimization — no scan detection or reactive emergency rotation. No physical hardware deployment. No TCP monitoring flow for scan visibility post-NAT.
"Effectiveness of Moving Target Defenses" Evans, Nguyen-Tuong & Knight Springer — Moving Target Defense, 2011 | Theoretically analyzes effectiveness of MTD approaches. Defines metrics for defense quality, attack surface reduction, and the cost-benefit tradeoff of randomization strategies. | Analytical study only — no SDN or network implementation. No scan detection. Metrics not validated against real attack tools or physical hardware deployment.
"Creating a Cyber Moving Target for Critical Infrastructure Applications" Okhravi, Comella, Robinson & Haines Computers & Security, Elsevier, 31(8), 2012 | MIT Lincoln Lab paper proposing MTD for critical infrastructure via platform diversity — rotating OS types, services, and addresses across nodes to make attacker reconnaissance persistently stale. | Targets platform heterogeneity, not SDN-based address mutation. No OpenFlow or controller-based NAT pipeline. No reactive scan detection or embedded hardware deployment.
"Optimal Strategy Selection for Moving Target Defense Based on Markov Game" Lei, Ma & Zhang IEEE Access, 2017 | Models the attacker-defender MTD interaction as a two-player Markov game. Derives Nash equilibrium rotation strategies that maximize defense while minimizing overhead cost. | Game-theoretic model only — no SDN or OpenFlow implementation. Cannot detect or react to active scans. Theory not validated in a live network or on physical hardware.

## Slide 10
TENTATIVE TIMELINE
Phase 1 — Literature Review · Early July 2026 30 papers surveyed; research gap identified (no reactive scan detection in existing MTD)
Phase 2 — System Design . July 2026 3-table OpenFlow NAT pipeline designed; VIP pool, rotation interval, and GPIO pin mapping decided
Phase 3 — Software Implementation . August 2026 Ryu controller, Mininet topology, scan detector, LED driver, and automated demo script built
Phase 4 — Partial Hardware Deployment · August 2026 (for Mid Review) System deployed on Raspberry Pi 5 with GPIO LEDs wired , however, it is still software running on a different cpu
Phase 5 — Full Hardware Deployment with Ethernet cables . September 2026 Presentation prepared; teacher feedback incorporated
Phase 6 — October 2026 Perfecting of Software and Hardware deployments, correcting any shortcomings or malfunctions.

## Slide 11
References (1 / 4)
NEW TO THIS SECTION — BACKGROUND & INFRASTRUCTURE
[1]
McKeown, N. et al. (2008). "OpenFlow: Enabling Innovation in Campus Networks." ACM SIGCOMM Computer Communication Review, 38(2), pp. 69-74.
OpenFlow's founding paper — the protocol our controller uses to push NAT rewrite rules into Open vSwitch at the data plane.
[2]
Lantz, B., Heller, B. & McKeown, N. (2010). "A Network in a Laptop: Rapid Prototyping for Software-Defined Networks." ACM HotNets-IX.
Introduced Mininet, the network emulator used in our simulation to run a complete virtual network on a single machine.
[3]
Pfaff, B. et al. (2015). "The Design and Implementation of Open vSwitch." USENIX NSDI, pp. 117-130.
Describes Open vSwitch — the software switch our controller programs via OpenFlow to enforce all VIP translation rules.
[4]
Kreutz, D. et al. (2015). "Software-Defined Networking: A Comprehensive Survey." Proceedings of the IEEE, 103(1), pp. 14-76.
Comprehensive SDN survey covering control-plane architecture and southbound protocols. Background for understanding our system design.
[5]
Postel, J. (1981). "Internet Protocol." IETF RFC 791.
The IPv4 specification — defines the packet format and addressing that our NAT rewrite rules operate on.

## Slide 12
References (2 / 4)
NEW TO THIS SECTION — BACKGROUND & INFRASTRUCTURE
[6]
Braden, R. (1989). "Requirements for Internet Hosts — Communication Layers." IETF RFC 1122.
Host communication requirements — relevant to how attacker hosts probe VIPs and how real hosts respond to TCP/ICMP.
[7]
Narten, T. et al. (2007). "Privacy Extensions for Stateless Address Autoconfiguration in IPv6." IETF RFC 4941.
IPv6 host-level address randomization — conceptual precursor to what our SDN controller does at the network layer for IPv4.
[8]
Scott-Hayward, S., O'Callaghan, G. & Sezer, S. (2013). "SDN Security: A Survey." IEEE Future Networks & Mobile Summit (SDN4FNS), pp. 1-7.
Survey of SDN-specific security threats and defenses — why the SDN controller is both a powerful defense tool and a high-value attack target.
[9]
Bellovin, S. M. (1989). "Security Problems in the TCP/IP Protocol Suite." ACM SIGCOMM Computer Communication Review, 19(2), pp. 32-48.
Foundational paper identifying inherent TCP/IP vulnerabilities — directly motivates why network-layer defenses like MTD are necessary.
[10]
Durumeric, Z., Wustrow, E. & Halderman, J. A. (2013). "ZMap: Fast Internet-Wide Scanning and its Security Implications." USENIX Security, pp. 605-619.
Shows how attackers can scan the entire IPv4 space in under an hour — the exact reconnaissance threat our VIP rotation is designed to defeat.

## Slide 13
References (3 / 4)
OTHER PAPERS MENTIONED IN PPT — RELATED WORK (Slides 9-10)
[11] Antonatos, S. et al. (2007). "Defending Against Hitlist Worms using Network Address Space Randomization." Computer Networks, Elsevier.
[12] Vikram, S. et al. (2011). "NOMAD: Towards Non-Intrusive Moving-Target Defense Against Web Bots." IEEE CNS.
[13] Cho, J. H. et al. (2020). "Toward Proactive, Adaptive Defense: A Survey on Moving Target Defense." IEEE Communications Surveys & Tutorials, 22(1), pp. 709-745.
[14] Shi, L. et al. (2017). "Effective Moving Target Defense for SDN-based Cloud Networks." IEEE TrustCom.
[15] Hong, J. B. & Kim, D. S. (2016). "Assessing the Effectiveness of MTD Using Security Models." IEEE Trans. on Dependable & Secure Computing.
[16] Zhuang, R., DeLoach, S. A. & Ou, X. (2014). "Towards a Theory of Moving Target Defense." ACM Workshop on Moving Target Defense (MTD '14), pp. 31-40.
[17] Peng, W., Li, F., Huang, C. T. & Zou, X. (2014). "A Moving-Target Defense Strategy for Cloud-Based Services with Heterogeneous and Dynamic Attack Surfaces." IEEE ICC 2014.
[18] Wang, H. et al. (2020). "Moving Target Defense for Internet of Things Using the MQTT Protocol." IEEE Access.
[19] Atighetchi, M. et al. (2003). "Adaptive Use of Network-Centric Mechanisms in Cyber-Defense." IEEE SRDS.
[20] Jafarian, J. H. et al. (2014). "Spatio-Temporal Address Mutation for Proactive Cyber Agility." ACM MTD Workshop.
[21] Paxson, V. (1998). "Bro: A System for Detecting Network Intruders in Real-Time." USENIX Security Symposium.
[22] Rowe, N. et al. (2006). "Fake Honeypots: A Defensive Tactic for Cyberspace." IEEE IAW.

## Slide 14
References (4 / 4)
OTHER PAPERS MENTIONED IN PPT — LITERATURE REVIEW (Slides 7-8)
[23] Jafarian, J. H., Al-Shaer, E. & Duan, Q. (2012). "OpenFlow Random Host Mutation: Transparently Moving Target Defense using SDN." ACM HotSDN.
[24] Jafarian, J. H., Al-Shaer, E. & Duan, Q. (2015). "An Effective Address Mutation Approach for Disrupting Reconnaissance Activities." IEEE Trans. on Information Forensics and Security, 10(12), pp. 2562-2577.
[25] Dunlop, M. et al. (2011). "MT6D: A Moving Target IPv6 Defense." IEEE MILCOM.
[26] Kampanakis, P., Perros, H. & Beyene, T. (2014). "SDN-based Solutions for Moving Target Defense Network Application." IEEE WoWMoM.
[27] Debroy, S., Calyam, P. & Nguyen, M. (2016). "Frequency-Minimal Moving Target Defense using SDN." IEEE ICNC.
[28] Evans, D., Nguyen-Tuong, A. & Knight, J. (2011). "Effectiveness of Moving Target Defenses." In: Moving Target Defense. Springer.
[29] Okhravi, H., Comella, A., Robinson, E. & Haines, J. (2012). "Creating a Cyber Moving Target for Critical Infrastructure Applications." Computers & Security, 31(8), pp. 879-887.
[30] Lei, C., Ma, D. H. & Zhang, H. Q. (2017). "Optimal Strategy Selection for MTD Based on Markov Game." IEEE Access.